## Slide 1: An IETF view of ENUM
Geoff Huston
Executive Director,
Internet Architecture Board
Presented at ICANN, Rio de Janiero, 2003
by Richard Stastny

## Slide 2: Who is the IETF?
Internet Engineering Task Force
The organization that oversees the standards process for Internet protocols and technologies
Industry-based standards body with broad participation from vendors, operators and researchers
We make standards that work – how you work them is up to you!

## Slide 3: The Structure of the IETF

## Slide 4: Huh? - Lets see that again!
Internet Society
IESG
IAB
RFC Editor
IANA
Areas (7)
Working Groups
IETF
IRTF

## Slide 5: How does the IETF Work?
We do not believe in Kings, Presidents and Voting. We believe in rough consensus and running code
Dave Clark, MIT, Former IAB member
The IETF has a focus on developing standards where interoperability testing of conformant implementations of the standard, and use of the technology in production contexts form an integral part of the standards process

## Slide 6: How Does the IETF Work?
Proposed work items are aired at a BOF session
  Gather interest and support
A work program is chartered by the IESG
  Working Group Charter
    WG Chair(s) and Area Director
    Working Group statement of activity
    Schedule of milestones
  Periodic IESG review and recharter as necessary

## Slide 7: IETF Documents
Internet Drafts
  http://www.ietf.org/1id-abstracts.html
  Individual submissions
    draft-<person>-<header>
  Working Group Documents
    draft-ietf-<working group>-<header>
    Working Group documents denote some level of ‘buy-in’ from the community of interest

## Slide 8: IETF Documents
RFCs
  Informational
  Best Current Practice
  Standards Track
    Proposed (good idea, clearly written, Working Group approved, peer reviewed)
    Draft (interoperability tested, sound idea)
    Full (many people are / were using this technology)
    Historic (no longer that useful)

## Slide 9: ENUM
ENUM is a working group with the IETF Transport Area

## Slide 10: ENUM (cont)

## Slide 11: ENUM (cont)

## Slide 12: Why ENUM?
Because tpc.int did not work!
  tpc.int (c 1992) mapped E.164 numbers to A records (IP addresses) to emulate fax delivery
  Each new service required a new E.164 -> IP address mapping
  Did not scale to multiple services using a single mapping
ENUM is part of a broader IETF approach of splitting out the components of VOIP / PSTN interaction into discrete efforts and addressing each component as a discrete technology standardization effort
ENUM is not an end in itself

## Slide 13: The Good Bits of ENUM
E164.arpa
  Single mapping that is service independent
  Each mapping can be associated with a collection of URIs
  The mapping may be statically configured or dynamically generated (or both)
  Each end point of the DNS hierarchy populates the entry with desired service entries
  Each application selects compatible service entries from the set
  ENUM is independent of directory, call control, routing and transport considerations
  Its just a mapping from the E.164 domain into multiple URI service domains

## Slide 14: The Not So Good Bit
The DNS is an issue in itself……
  DNS is insecure
    TSIG, DNSSEC, PKI, etc may help, but when and how much?
  DNS is variably timed
  DNS is generally not well maintained
  DNS is generally not well synchronized
  There is no “DNS says ‘no’”, only an indistinct timeout
  Putting regular expressions in the DNS is an fascinating complication
  But we have nothing better in terms of a very large distributed database to poke towards this problem space
  Remember:
  The DNS is a lousy kitchen sink. We have seen many proposals to “just put it in the DNS”. Be very concerned whenever you hear this!

## Slide 15: ENUM is NOT everything
In particular, ENUM is NOT:
  a directory
  a search service
  a transport service
  a voice encoding method
  a rendezvous protocol
All ENUM is a distributed partial mapping from E.164 addresses into a set of service points identified via a URI labelling

## Slide 16: The VOIP Gateway Model for enum
Most IETF work these days assumes a ‘reference architecture’
ENUM’s core reference architecture is VOIP-to-VOIP
PSTN
Internet
VOIP Server
VOIP Served subnet
Enum Service Point

## Slide 17: The Gateway VOIP Model
The single gateway model is simple:
  A PSTN / IP gateway maintains a mapping between IP and E.164 addresses
VOIP
Gateway
IP Net
PSTN
10.0.0.10 12345678
10.0.0.11 12345679
10.0.0.12 12345680
IP E.164
1. Call “12345678”
2. PSTN routes the call to 12345678 to the VOIP gateway
3. Gateway maps E.164 address “12345678” to IP 10.0.0.10
4. Gateway initiates a SIP session with 10.0.0.10
12345678
10.0.0.10

## Slide 18: The multi-Gateway VOIP World
Use PSTN / VOIP Gateways
  Each Gateway maps a set of telephone numbers to a set of served IP service addresses
  Each Gateway knows only about locally served devices
  Gateway-to-Gateway calls need to be explicitly configured in each gateway to use IP or some private connection, or use the default of the PSTN
  The PSTN currently is the glue that allows the VOIP islands to interconnect with each other

## Slide 19: The multi-Gateway VOIP World
VOIP Islands
  E.164 numbers are only routable over the PSTN
  Enterprise or carrier VOIP dialling plans cannot be remotely accessed by other VOIP network segments
PSTN
Internet

## Slide 20: The Core ENUM Problem
How can a VOIP gateway find out dynamically:
  If a telephone number is reachable as an Internet device?
  And if so, what’s its Internet service address?
PSTN
Internet

## Slide 21: Problem statements for ENUM (1)
How do network elements (gateways, SIP servers etc) find services on the Internet if you only have a telephone (E.164) number?

## Slide 22: Problem statements for ENUM (2)
How can subscribers define their preferences for nominating particular services and servers to respond to incoming communication requests?

## Slide 23: The ENUM Objective
Allow any IP device to establish whether an E.164 telephone address is reachable as an Internet-described Service
  And … what the preferred Service Point actually is
  And if its an Internet-reachable Service Point… what IP address, protocol address, port address and application address should be used to contact the preferred Service Point

## Slide 24: ENUM Resolution
The PSTN is a multi-service platform
To emulate this in IP, IP services associated with a single E.164 may be provided on a collection of different IP service points
An ENUM DNS request should return the entire set of service points and the associated service.
DNS
Selection
DNS
Connection
E.164 address
Set of URIs
.
.
.
.
URI
IP Address
TCP/UDP Port
Protocol Address

## Slide 25: Why URIs?
URIs represent a generic naming scheme to describe IP service points
  Generic format of
  service:service-specific-address
A URI in IP context is ultimately resolvable to
  transport protocol (TCP/UDP) selection
  IP address
  Port address
  Address selector within the application session

## Slide 26: The Longer Term
Telephone numbers are well accepted identifiers within their realm of application
Any collection of service URIs can be linked against an ENUM entry
  mail, www, irc, sms,…

## Slide 27: E.164 as a common address substrate ?
Use this number for any service
+61 2 12345678
ENUM
sip:gih@sip.telstra.net
tel:+61 2 62486165
mailto:gih@telstra.net
tel:+61 2 12345678

## Slide 28: Practical Issues
Issues where the IETF has an active interest…
  Who should manage the e164.arpa zone?
  Should there be one root for a single ENUM database or multiple databases for different functions, number ranges, area codes or even numbers?
  How to secure the DNS to ensure that ENUM answers are valid, timely and authoritative

## Slide 29: Practical Issues
Issues where the IETF has a limited (if any) role to play in ENUM
  How to protect the privacy of the ENUM database?
  How to verify changes to the ENUM database?
  Should telephone number holders ‘opt-in’ or ‘opt-out’ of the system?
  Portability and ownership of a phone number?
    Can I cancel all phone services and keep my phone number?
  Compliance with legislative framework
    What is a “public telephone call” from a strict regulatory perspective?
  Is there a valid need for yet another public identity space?